## Slide 1
PYTHON · SIMPY · SATELLITE TOLLING
GPS Toll-Based System Simulation
Pay only for the kilometres you drive: distance-based tolling on the Coimbatore → Bangalore highway
362 km
real road route
8
real toll plazas
−24%
toll for a car
github.com/Kes2003/gps-toll-system
Notes: Good morning. Our project is a GPS toll-based system simulation. Today, highway tolls in India are charged at plazas: you pay a fixed fee at each plaza you pass, however much of the road you use. We simulate the alternative the government is moving towards: satellite-based, distance-based tolling, where your GPS track decides the toll. We built it on the real 362 km Coimbatore to Bangalore highway, with its 8 real toll plazas and their published fees.

## Slide 2
GPS Toll-Based System Simulation
2 / 17
THE PROBLEM
Plaza tolls charge the full fee, however far you drive
One fixed fee per plaza
Each plaza charges a single fee for its whole section, 10 to 86 km on this route, even if you drive only part of it.
Distance isn't measured
What you pay depends on which plazas you pass, not on the kilometres you actually use.
Short trips pay the most per km
A local trip through one plaza pays exactly what a long-distance trip through that section pays.
EXAMPLE TRIP
Krishnagiri → Hosur by car
₹95
FASTag: the plaza's full fee
₹22
GNSS: 51 km actually driven
Simulated with NHAI's published fees and the 20 km free rule.
Notes: Here is the problem. A toll plaza charges one fixed fee for a whole section of highway, between 10 and 86 km on our route. The fee doesn't depend on how much of that section you drive. For example, a car going from Krishnagiri to Hosur, 51 km, pays the full 95 rupee fee at the Krishnagiri plaza. Charged by distance, with the first 20 km free, the same trip costs about 22 rupees.

## Slide 3
GPS Toll-Based System Simulation
3 / 17
PROJECT OBJECTIVES
Every requirement in the brief, delivered
01
Define toll zones
Each real plaza's tollable length becomes a toll zone on the 362 km route.
Delivered
02
Register entry and exit
GPS fixes are snapped to the road; zone entry and exit are logged with time and km.
Delivered
03
Calculate distance and toll
Km in each zone × that plaza's rate, with the 20 km free rule and a FASTag comparison.
Delivered
04
Display the path
Route and traffic charts, toll by plaza, and an interactive map of every GPS track.
Delivered
BEYOND THE BRIEF
Multi-vehicle traffic
GPS noise and varying speed
Real NHAI toll fees
SQLite trip history
66 automated tests
Notes: Our brief had four requirements: define toll zones, register where the vehicle enters and leaves them, calculate the distance and the toll, and display the vehicle's path. All four are delivered, and we went further: many vehicles at once, realistic GPS error and speed, real NHAI fees, a trip history database, and 66 automated tests.

## Slide 4
GPS Toll-Based System Simulation
4 / 17
OUR SOLUTION
Satellite-based tolling, simulated end to end
Instead of charging at plazas, the vehicle's GPS track decides the toll.
Track
A GPS fix every 10 seconds, with realistic error, snapped back onto the road.
Detect
Entry into and exit from each toll zone, registered from the vehicle's position.
Charge
Kilometres in each zone × that plaza's own per-km rate. The first 20 km a day are free.
Record
An itemised receipt, the FASTag cost for comparison, and a SQLite trip history.
Modelled on India's National Highways Fee Amendment Rules, 2024, which allow GNSS-based toll collection.
Notes: Our solution simulates satellite-based tolling from start to finish. First, track: the vehicle reports a GPS fix every 10 seconds. Second, detect: we register when it enters and leaves each toll zone. Third, charge: it pays for the kilometres it drove in each zone, at that plaza's own rate, with the first 20 km free as the 2024 rules allow. Fourth, record: an itemised receipt, the FASTag comparison, and a permanent trip history.

## Slide 5
GPS Toll-Based System Simulation
5 / 17
HOW IT WORKS
From GPS fix to toll receipt
STEP 1
Depart
Your vehicle and random traffic leave their towns.
STEP 2
Drive
Speed drifts around each vehicle's cruising speed.
STEP 3
GPS fix
Every 10 s, with about 5 m of random error.
STEP 4
Map-match
Each fix is snapped to the nearest point on the road.
STEP 5
Detect zones
Crossing a zone boundary logs an entry or exit.
STEP 6
Bill and save
Receipt issued and the trip saved to SQLite.
TOLL FORMULA
Toll = Σ (km driven in zone × plaza fee ÷ tollable length) − first 20 km free
Notes: This is the pipeline for every vehicle, running in a SimPy discrete-event simulation. Vehicles depart from their towns and drive at a speed that drifts naturally. Every 10 seconds we take a GPS fix with a few metres of random error, and snap it back onto the road, which is called map-matching. When the matched position crosses a zone boundary we log an entry or an exit. At the destination the bill is calculated with this formula, a receipt is issued, and the trip is saved.

## Slide 6
GPS Toll-Based System Simulation
6 / 17
REAL DATA
A real 362 km corridor with 8 toll plazas
Toll plaza | Zone (km) | Car fee | ₹ / km
Kaniyur | 2.6 – 45.3 | ₹125 | 2.93
Vijayamangalam | 48.3 – 96.8 | ₹65 | 1.34
Vaiguntham | 106.3 – 148.6 | ₹75 | 1.40
Omalur | 148.6 – 186.1 | ₹95 | 1.38
Thoppur | 186.1 – 248.5 | ₹160 | 1.86
Krishnagiri | 248.5 – 304.6 | ₹95 | 1.59
Attibele | 322.3 – 336.7 | ₹35 | 2.43
Electronic City | 338.5 – 348.5 | ₹60 | 6.00
Road geometry and plaza positions from OpenStreetMap. Fees and tollable lengths from NHAI's Toll Information System.
Notes: We didn't use a straight line. The route is the real road from OpenStreetMap: NH544 to Salem, then NH44 through Dharmapuri, Krishnagiri and Hosur, 362 km in total. There are 8 real toll plazas on it, with their published NHAI fees. Each plaza's tollable length becomes an orange toll zone on the map, and its per-km rate is simply its fee divided by that length. Rates range from 1.34 rupees per km to 6 rupees on the Electronic City elevated road.

## Slide 7
GPS Toll-Based System Simulation
7 / 17
WORKED EXAMPLE
A car from Coimbatore to Bangalore pays 24% less
Chart: Toll by plaza (₹)
| Electronic City | Attibele | Krishnagiri | Thoppur | Omalur | Vaiguntham | Vijayamangalam | Kaniyur
GNSS (distance based) | 60 | 35 | 89.03 | 115.99 | 51.95 | 59.3 | 65 | 66.36
FASTag (full plaza fee) | 60 | 35 | 95 | 160 | 95 | 75 | 65 | 125
₹542.63
GNSS toll: 313.8 km in toll zones
₹710
FASTag: full fee at all 8 plazas
First 20 km a day free
NH Fee Amendment Rules, 2024
No free km for National Permit trucks
3-axle and larger goods vehicles
Notes: Here is a real example from the simulation: a car driving the whole route. In blue is what it pays with distance-based tolling, in orange what it pays at FASTag plazas today. Where the car drives a plaza's whole section, the two match, as at Attibele and Electronic City. Where zones overlap or the first 20 free kilometres apply, GNSS is cheaper. In total the car pays 542 rupees instead of 710, which is 24% less.

## Slide 8
GPS Toll-Based System Simulation
8 / 17
INSIGHT
Short trips see the biggest difference
UP TO
77%
less toll on short trips
Krishnagiri → Hosur by car: ₹22 instead of ₹95. You pay for the 51 km you drive, not for the plaza's whole section.
Salem → Dharmapuri: ₹77 instead of ₹255.
Chart: Car toll for short trips (₹)
| Hosur → Bangalore (40 km) | Krishnagiri → Hosur (51 km) | Salem → Dharmapuri (62 km) | Coimbatore → Avinashi (44 km)
GNSS (distance based) | 23.31 | 22.06 | 76.59 | 61.76
FASTag (full plaza fee) | 95 | 95 | 255 | 125
Notes: The biggest difference is on short trips. Local drivers crossing one plaza pay its full fee today. With distance-based tolling they pay only for what they drive, and the first 20 km are free. Krishnagiri to Hosur drops from 95 rupees to 22, Salem to Dharmapuri from 255 to 77. That is up to 77% less.

## Slide 9
GPS Toll-Based System Simulation
9 / 17
FLEET SIMULATION
Many vehicles on the highway at once
TRAFFIC MIX
Chart: 
| Oversized (7+) | 3-axle | Bus / Truck | LCV / Mini bus | Multi-axle (4–6) | Car / Jeep / Van
Share of traffic | 5 | 7 | 8 | 12 | 13 | 55
Speed drifts ±10% around each vehicle's cruising speed
About 5 m of GPS error, corrected by map-matching
Departures spread over two hours, from 9 towns
Notes: Real highways carry mixed traffic, so we simulate many vehicles at once. Each line in this time-distance chart is one vehicle: its slope is its speed, and the shaded bands are the toll zones. Traffic follows a realistic mix, 55% cars with LCVs, buses and trucks, joining and leaving at 9 towns. Speeds drift naturally, and GPS fixes carry a few metres of error that map-matching corrects.

## Slide 10
GPS Toll-Based System Simulation
10 / 17
RESULTS
200 vehicles, 31,663 km: 23% less toll overall
₹1,18,247
GNSS tolls for all 200 vehicles
₹1,53,525
FASTag plaza fees for the same trips
165 of 200
vehicles pay less with GNSS
Chart: Full Coimbatore → Bangalore trip by vehicle class (₹)
| Car | LCV | Bus / Truck | 3-axle | 4–6 axle | 7+ axle
GNSS (distance based) | 542.63 | 885.59 | 1808.67 | 3078.15 | 3266.64 | 3679.15
FASTag (full plaza fee) | 710 | 1160 | 2370 | 3600 | 3860 | 4330
Heavy goods vehicles hold National Permits, so they get no free 20 km and save about 15%.
Notes: We ran 200 vehicles with a fixed random seed: 31,663 km of driving. Distance-based tolls came to 1.18 lakh rupees against 1.54 lakh at FASTag plazas, 23% less, and 165 of the 200 vehicles paid less. On the right, the full route by vehicle class: cars, LCVs and buses save about 24%. Heavy trucks save about 15%, because National Permit vehicles don't get the free 20 km.

## Slide 11
GPS Toll-Based System Simulation
11 / 17
THE APPLICATION
A desktop app and a command-line tool
Tkinter GUI
Choose vehicle, towns, traffic and GPS noise; see every vehicle in one table.
Command line
python main.py --cli --traffic 20 for scripted, repeatable runs.
Charts
Route and toll zones, time-distance traffic, and toll by plaza.
Interactive map
Every GPS track, zone entries and exits, and each plaza's fee table.
Receipts and history
Itemised receipts, with every trip stored in SQLite.
Notes: The project runs as a desktop app or from the command line. In the app you choose the vehicle type, the towns, how much other traffic to add and the GPS error, then press Start. Every vehicle appears in the results table. Selecting one shows its itemised toll, its charts, the interactive map and its receipt. Every trip is saved to the database automatically.

## Slide 12
GPS Toll-Based System Simulation
12 / 17
ARCHITECTURE
Four clear layers, one job per module
Interfaces
How users run it
main.py
Command line
gui.py
Tkinter desktop app
Output
What users see
visualization.py
Matplotlib charts, Folium map
billing.py
Itemised receipts
storage.py
SQLite trip history
Core
The simulation
simulation.py
SimPy fleet, speed, GPS
tolling.py
Toll zones and bill
models.py
Route, map-matching
rates.py
Vehicle classes
Data
Real inputs and records
route.json
OpenStreetMap road
toll_plazas.json
NHAI fees and lengths
trips.db
Saved trips and charges
Notes: The code is organised in four layers. Interfaces: the command line and the Tkinter app. Output: charts and map, receipts, and the SQLite history. Core: the SimPy simulation, the toll zone and billing logic, the route model with map-matching, and the vehicle classes. Data: the real route and plaza files, plus the trip database. Each module has one job, which kept it easy to test.

## Slide 13
GPS Toll-Based System Simulation
13 / 17
TECHNOLOGY
Built with proven open-source tools
Python 3.9+
Language; tested on 3.11 and 3.12
SimPy
Discrete-event simulation of every vehicle
Geopy
Geodesic distances along the road
Matplotlib
Route, traffic and toll charts
Folium
Interactive Leaflet map in the browser
SQLite
Trip and toll charge history
Tkinter
Desktop user interface
pytest
66 automated tests
OpenStreetMap
Real road (via OSRM) and plaza positions
Notes: Everything is built with open-source Python tools: SimPy for the simulation, Geopy for distances, Matplotlib and Folium for charts and the map, SQLite for the history, Tkinter for the interface and pytest for testing. The road data comes from OpenStreetMap through the OSRM routing engine.

## Slide 14
GPS Toll-Based System Simulation
14 / 17
CREDIBILITY
Real data, verified by tests
66
automated tests, all passing
Map-matching and the real route data
Toll zones, 20 km rule and National Permits
Noisy and noise-free GPS bill the same
Fleets, partial trips, receipts and SQLite
Charts, map and command line
DATA SOURCES
OpenStreetMap + OSRM
Road geometry, towns and toll booth positions (ODbL licence).
NHAI Toll Information System
Fees for 6 vehicle classes and the tollable length of all 8 plazas.
NH Fee Rules, 2008
Vehicle classes and base per-km rates.
NH Fee Amendment Rules, 2024
GNSS tolling with the first 20 km a day free.
Notes: Two things make these results trustworthy. The data is real: OpenStreetMap for the road, NHAI's published fees for every plaza, and the actual fee rules including the 2024 amendment. And the code is tested: 66 automated tests, including a check that noisy GPS produces the same bill as perfect GPS.

## Slide 15
GPS Toll-Based System Simulation
15 / 17
TEAM
Team members and contributions
Team Member 1
Project lead · Simulation
SimPy fleet simulation, toll zone logic and integration.
Team Member 2
GPS · Route data
OpenStreetMap route, map-matching and distance calculation.
Team Member 3
Database · Billing
SQLite trip history, receipts and NHAI fee data.
Team Member 4
Frontend · GUI
Tkinter app, charts and the interactive map.
Notes: Each team member introduces their own part here. Replace 'Team Member 1' to 4 with your names before presenting.

## Slide 16
GPS Toll-Based System Simulation
16 / 17
WHAT'S NEXT
Limitations and roadmap
TODAY
NEXT STEP
One direction: Coimbatore → Bangalore
Reverse the route for return trips
Toll zones centred on each plaza
Use official section start and end chainages
20 km free applied per trip
Track the free allowance per vehicle per day
Fees are a 2025–26 snapshot
Refresh fees from NHAI every year
No congestion or GPS signal loss
Add traffic density and GPS outages
Notes: Like any simulation, ours has limits, and each has a clear next step. Vehicles only drive towards Bangalore; the return direction is the obvious next step. Zones are centred on each plaza because official section boundaries aren't published in the data we used. The free 20 km is applied per trip rather than per day. Fees are a snapshot that NHAI revises yearly. And there is no congestion model yet.

## Slide 17
GPS Toll-Based System Simulation
17 / 17
CONCLUSION
Pay for the road you actually use
24%
less toll for a car driving the full 362 km route
77%
less on short trips such as Krishnagiri → Hosur
8
real plazas with real fees, on a real road
Thank you
Questions?
github.com/Kes2003/gps-toll-system
Notes: To conclude: distance-based tolling charges drivers for the road they actually use. In our simulation of the real Coimbatore to Bangalore highway, a car pays 24% less for the full route, and short local trips pay up to 77% less. Everything is built on real roads, real plazas and real fees, and the code is on GitHub. Thank you, we're happy to take questions.